Proposal for corrigendum to (ECE/TRANS/WP.29/2010/23)

The modification to text is based on document ECE/TRANS/WP.29/2010/23 submitted for adoption to WP.29 and AC.1 by the Working Party on Lighting and Light-Signalling.  The corrigendum is aimed at avoiding misinterpretation of the transitional provisions of draft Supplement 5 to the 04 series of amendments to Regulation No. 48.  As a matter of fact, at its October 2009 session, GRE adopted ECE/TRANS/WP.29/GRE/2009/34 including transitional provisions reported in paragraph 12.21. These provisions referred only to the automatic switching and their alternatives of the dipped beam headlamps installed on a vehicle equipped with daytime running lamps and not to all provisions of Supplement 5.  Accordingly, the text of transitional provisions should be amended as follows:

Page 8, paragraph 12.21., amend to read:

"12.21.	As from 48 months from the official date of entry into force of Supplement 5 to the 04 series of amendments, Contracting Parties applying this Regulation shall grant approvals only if the vehicle type to be approved meets the requirements of paragraphs 6.2.7.6. to 6.2.7.6.3.3. of this Regulation as amended by Supplement 5 to the 04 series of amendments."

- - - - -