Proposal for draft Corrigendum 1 to the 05 series of amendments of Regulation No. 48

(Installation of lighting and light-signalling devices)

A. 	PROPOSAL

Paragraph 6.9.8., amend to read:

"6.9.8.	Circuit-closed tell-tale mandatory. […] with the front position lamps.

This requirement does not apply when light signalling system operates according to 6.2.7.6.2.

Paragraph 6.10.8., amend to read:

"6.10.8.	Circuit-closed tell tale mandatory. It must be combined with that of the front position lamps.

This requirement does not apply when light signalling system operates according to 6.2.7.6.2."

B. 	JUSTIFICATION

In the 05 serie of ECE 48 it is possible to use daytime running lamps operating in conjunction with at least the rear position lamps as an alternative to the sensor.

The use of the position lamps in conjunction with daytime running lamps could lead to interpret that the tell tale should be activated as it is now the case in the "traditional use" of the position lamps.

As in this case the position lamps are only an alternative to the sensor it should be clarify that this is not mandatory and it was not the aim of the proposal.

So we made this proposal to clarify the situation.