|  | United Nations | ECE/TRANS/WP.29/2011/72 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 1 April 2011 English Original: English and French |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

154th session

Geneva, 21–24 June 2011

Item 4.12.1 of the provisional agenda

1958 Agreement – Consideration of draft corrigenda

to existing Regulations submitted by GRRF

Proposal for Corrigendum 1 to Supplement 9 to Regulation No. 13-H (Brakes of M1 and N1 vehicles)

Submitted by the Working Party on Brakes and Running Gear*

The text reproduced below was adopted by the Working Party on Brakes and Running Gear (GRRF) at its sixty-ninth session to correct brake assist requirements. It is based on ECE/TRANS/WP.29/GRRF/2011/5, as superseded by Annex IV to the report (ECE/TRANS/WP.29/GRRF/69, para. 17). It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration.

Paragraphs 2.34.1 and 2.34.2., amend to read (with the addition of a new footnote*):

"2.34.1.	"Category A Brake Assist System" means a system which detects an emergency braking condition based primarily* on the brake pedal force applied by the driver;

2.34.2.	"Category B Brake Assist System" means a system which detects an emergency braking condition based primarily* on the brake pedal speed applied by the driver;"

Paragraph 2.34.3., shall be deleted.

Annex 1

Paragraph 22.1., amend to read:

"22.1. 	Category of Brake Assist System A / B 2/"

Paragraph 22.1.3., shall be deleted.

Annex 9, section B

Paragraph 1.2., amend to read:

"1.2.	General performance characteristics for category "B" BAS systems

When an emergency… met."

Paragraph 2.1.6., amend to read:

"2.1.6	Brake pedal speed, vp, measured at the centre… the measurement."

Paragraphs 5. to 5.2., shall be deleted.

Annex 9, Appendix 4

Paragraph 1.2., amend to read:

"1.2.	The brake pedal… (without activating the BAS in the case of category B systems) providing… cycling (Figure 3)."

Paragraph 1.3., amend to read:

"1.3.	The full deceleration… 2 seconds. Once full deceleration has been achieved, the brake pedal shall be operated so that the ABS continues fully cycling. The time of full activation… in deceleration (see Figure 3)."

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208/, para. 106 and ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.

*	as declared by the vehicle manufacturer.