|  | United Nations | ECE/TRANS/WP.29/2012/72 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 27 July 2012 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

158th session

Geneva, 13-16 November 2012

Item 4.7.11 of the provisional agenda

1958 Agreement – Consideration of draft amendments

to existing Regulations submitted by GRE

Proposal for Supplement 7 to the 01 series of amendments to Regulation No. 45 (Headlamp cleaners)

Submitted by the Working Party on Lighting and Light-Signalling*

The text reproduced below was adopted by the Working Party on Lighting and Light-Signalling (GRE) at its sixty-seventh session to correct and harmonize the provisions concerning approval markings. It is based on ECE/TRANS/WP.29/GRE/2012/9, not amended (see ECE/TRANS/WP.29/GRE/67, para. 29). It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee AC.1 for consideration.

Annex 3, Figures 1and 2, amend to read:

"	Annex 3

Arrangements of the approval marks

I. 	Arrangement of the approval mark for a headlamp cleaner

The above approval mark … as amended by the 01 series of amendments.

Note: The approval number … , in order to prevent any confusion with other symbols.

II.	 Arrangements of approval marks for a vehicle with regard to headlamp cleaners

The above approval mark … as amended by the 01 series of amendments. The capacity class is 50.

The above approval mark … The capacity class is 50.

"

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106, ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.

# Text boxes

a = 5 mm min

a = 5 mm min

a = 5 mm min