## Slide 1
NEW TRACTION DEFINITION
GRBP 70th session
Document GRBP-70-19
Agenda items 6 and 14

## Slide 2
CURRENT TRACTION DEFINITION (reminder)
[...]
2.12. “Traction tyre” means a tyre in class C2 or C3 bearing the inscription TRACTION and intended to be fitted primarily to the drive axle(s) of a vehicle to maximize force transmission in various circumstances.
6.5.1. The tyre shall have a tread pattern with minimum two circumferential ribs,
each containing a minimum of 30 block-like elements, separated by grooves and/or sipe elements, the depth of which has to be minimum of one half of the tread depth.
The use of an alternative option of a physical test will only apply at a later stage following a further amendment to the Regulation including a reference to an appropriate test methods and limit values.
(CURRENT) DEFINITION OF TRACTION IS BASED ON 1 GEOMETRICAL PATTERN PARAMETER
 2012 : ETRTO TRACTION TASK FORCE WAS FIRSTLY LOOKING FOR A TEST METHOD(S) AS ALTERNATIVE OPTION

## Slide 3
3 full Round Robin Tests
8 types of patterns, 12 tyre candidates
34 soil types tested by Companies during 2 years
  summer and winter campaigns
  21 EU tracks + 13 JPN tracks
  Sand, Clay, Loose soil, Gravel, Concrete, Metallic plates,...
  Wet and Dry tracks, Snow,...
TEST TRIALS (2013-2015)
TEST REPRODUCTIBILITY IS VERY LOW ESPECIALLY FOR SOFT SOILS.
AN ALTERNATIVE FOR NEW DEFINITION USING A UNIQUE OR A COMBINATION OF TEST(S) WAS NOT POSSIBLE

## Slide 4
Have a more objective correlation with performance
Use objective but simple measurements
Interest of a transversal void/fill ratio introduction
More precise definition of pattern traction elements
Take into account non rib patterns
Take into account future possible technologies and designs
ETRTO GUIDELINES for NEW APPROACH (2016)
 2016 : ETRTO TRACTION TASK FORCE WAS THEN LOOKING FOR A NEW APPROACH
 CHANGE FROM CURRENT PURE GEOMETRICAL APPROACH TO A MORE MECHANICAL APPROACH

## Slide 5
INTRODUCTION OF PATTERN “DEFORMATION POTENTIAL” CONCEPT
3 PARAMETERS : TOTAL AMOUNT of ELEMENTS & VOID/FILL RATIO & TREAD DEPTH.
NEW APPROACH IS MORE MECHANICAL ORIENTED ...
CURRENT DEFINITION
(only 1 factor)
NEW DEFINITION PROPOSAL
(3 factors)
Total amount of elements (TE)
Limit : 60 = minimum 2 x 30 elements
Total amount of elements (TE)
Deformation Potential (DP) =
void/fill ratio x tread depth 3
Introduction
of new concept of Deformation Potential
(deeper block and more voids lead to more deformation)
Image source :
Google image

## Slide 6
MORE FLEXIBILITY BUT MORE SEVERE CONDITION FOR BLOCK SEPARATION FEATURES
Stronger requirements concerning the separating grooves/sipes
from 50% to 70% and never below 10%
NEW APPROACH IS MORE MECHANICAL ORIENTED ... and MORE SEVERE (for longer Traction sustainability)
BUT STILL CLEAR, RELIABLE and without need of specific testing.
CURRENT DEFINITION
NEW DEFINITION
Elements separated
by grooves/sipes having
their depth
min 50% of tread depth
Elements separated
by grooves/sipes having
their depth in average
min 70% of tread depth AND everywhere min 10% of tread depth
min 10% TD

## Slide 7
TE : Total amount of Elements in tread pattern
DP : Pattern Deformation Potential = VR * TD 3 RD : Nominal Rim Diameter code
NEW TRACTION LIMITS
C2 - SMALL C3 - BIG C3
TE
400
200
100
60
0 500 1250 1400 2000 DP
TE
400
200
100
60
0 500 1250 1400 2000 DP
TE
400
200
100
60
0 500 1250 1400 2000 DP
C2 tyres
HERE ABOVE
MAY BE
TRACTION
Small C3 tyres with RD < 20
HERE ABOVE
MAY BE
TRACTION
Big C3 tyres with RD ≥ 20
HERE ABOVE
MAY BE
TRACTION
BELOW
MAY NOT
BELOW
MAY NOT
BELOW
MAY NOT
NEW LIMIT PROPOSALS

## Slide 8
Chart: 
| Existing definition | New definition proposal
May be | 75 | 40
May NOT be | 25 | 60
Chart: 
| Existing definition | New definition proposal
May be | 60 | 40
May NOT be | 40 | 60
SYNTHESIS : IMPACT on the MARKET DISTRIBUTIONS
Sales information :
2016 Europool data
With new TRACTION definition
Segregation will better correspond to market reality AND TO REGULATION INTENTION
C3 TYRES
C2 TYRES
CURRENT
Definition
60% might be
Traction marked -
40% may not be
NEW
Definition
Proposal
40% may be -
60% may
no more be
CURRENT
Definition
75% might be
Traction marked -
25% may not be
NEW
Definition
Proposal
40% may be -
60% may
no more be

## Slide 9: CONCLUSION
ETRTO considers that current TRACTION definition is not well segregating real Traction tyres from non-Traction ones.
It has not been possible to define a unique test method and a unique threshold to propose a physical test method.
ETRTO proposes a more mechanical approach for the new Traction definition.
This new Traction definition proposal provides a more accurate segregation, better corresponding to market reality.
Sufficient transitional provisions will be precised in a Working Document for next GRBP session if this proposal is accepted.

## Slide 10
Thank you ! !